Assessment of the
Statistical Impedance Field Method
for the Analysis of the RTN Amplitude
in Nanoscale MOS Devices
G. Torrente*, N. Castellani*, A. Ghetti☨ , C. Monzio Compagnoni*,
A. Lacaita*, A. S. Spinelli* and A. Benvenuti☨
* Politecnico di Milano, Milano, Italy
☨ Micron Technology Inc., Process R&D, Agrate Brianza, Italy

---
Outline
- Introduction
- Statistical Impedance Field Method (sIFM) for the analysis of the amplitude of RTN fluctuations
- Comparison between sIFM and conventional MC results
- Conclusions

---
Random Telegraph Noise
RTN is a fluctuation of device VT (or ID) between two definite levels
Technology scaling has been increasing the amplitude of RTN fluctuations giving rise to a wider statistical distribution

---
Statistical RTN effect
The fluctuation is due to a carrier capture/emission mechanism at the SiO2/Si interface
The RTN amplitude is the result of trap capability to stop the percolative path
RTN now represents a major reliability issue
source
drain
High VT
Low VT
Gate
Substrate
SiO
2

c

e

---
Conventional RTN MC scheme
The computational burden is proportional to the number of samples
Numerical implementation of a random atomistic doping configuration
Poisson/DD
solution
Random placement of a charge –q over the channel
Poisson/DD
solution
VG
VG

---
Statistical Impedance Field Method
Motivation: reducing the computational loads
Hypothesis: treating the variability sources as a small perturbation of Poisson/DD solution
Approximation: linear approximation of Poisson/DD equations around a reference condition
Thesis: treating the effects of variability sources through the Green Functions approach

---
Statistical Impedance Field Method
Literature: neutral VT statistics
This work: neutral VT statistics + RTN amplitude, using
sIFM-doping: atomistic doping as perturbation of the continuous doping case (with neutral and charged trap)
sIFM-trap: trapped charge as perturbation of the atomistic doping
size 12{δI rSub { size 8{k} } = Int {G rSub { size 8{D} } rSup { size 8{0} } \( r \) δN rSub { size 8{k} } \( r \) d rSup { size 8{3} } r} } {}
size 12{δN rSub { size 8{k} } \( r \) =N rSub { size 8{k} } \( r \) - N rSub { size 8{ ital "cont"} } \( r \) } {}

---
1- The sIFM-doping scheme
Continuous
doping
device
Calculation of δI
for the k-th doping
configuration:
size 12{G rSub { size 8{D} } rSup { size 8{0} } \( r \) } {}
alignl { stack { size 12{δI rSub { size 8{k} } = Int {G rSub { size 8{D} } rSup { size 8{0} } \( r \) δN rSub { size 8{k} } \( r \) d rSup { size 8{3} } r} } {} # δN rSub { size 8{k} } \( r \) =N rSub { size 8{k} } \( r \) - N rSub { size 8{ ital "cont"} } \( r \) {} } } {}
Iter. over bias points
Iter. over trap positions
Random
placement of
a charge –q
at the channel
surface
Calculation of δI
for the k-th doping
configuration:
size 12{G rSub { size 8{D} } rSup { size 8{ - {}} } \( r \) } {}
alignl { stack { size 12{δI rSub { size 8{k} } = Int {G rSub { size 8{D} } rSup { size 8{ - {}} } \( r \) δN rSub { size 8{k} } \( r \) d rSup { size 8{3} } r} } {} # δN rSub { size 8{k} } \( r \) =N rSub { size 8{k} } \( r \) - N rSub { size 8{ ital "cont"} } \( r \) {} } } {}
Iter. over bias points
Iter. over doping cases
Iter. over doping cases

---
2- The sIFM-trap scheme
Iter. over trap positions
Random
configuration of
atomistic doping
Calculation of δI
for the i-th trap:
size 12{δI rSub { size 8{i} } = ital "qG" rSub { size 8{T} } rSup { size 8{0} } \( r rSub { size 8{i} } \) } {}
Iter. over bias points
Iter. over doping cases
size 12{G rSub { size 8{T} } rSup { size 8{0} } \( r \) } {}

---
Computational load comparison
Given:
Ndop atomistic doping configurations
Ntrap trap positions per cell
Any simulation set gives a statistical ensamble of Ndop x Ntrap elements
Reference MC
sIFM-doping
sIFM-trap
(Ntrap+1) Poisson/DD solutions
(Ndop) Poisson/DD solutions
Ndopx(Ntrap+1) Poisson/DD solutions

---
Statistical dispersion of VT
W=L=32nm
tox=8nm
Na=2x1018cm-3
Both of the sIFM schemes are able to reproduce the reference MC statistics
Reduced computational burdens allow to explore lower probability ranges

---
A more in-depth analysis
A point by point comparison between MC and sIFM methods shows a non-negligible discrepancy in the results
Unphysical negative DVT may occur using sIFM-doping method
Correlation values are calculated omitting unphysical points
ρ=0.90
ρ=0.86

---
Role of trap position
Largest errors using sIFM schemes occur when the RTN trap is placed close to cell edges
Dispersion is symmetric over the average value
VT estimation errors compensate each other in a statistical analysis

---
Vertically non-uniform dopings
In some cases sIFM schemes maybe inaccurate also for DVT statistics
The sIFM-trap is not very inaccurate
The sIFM-doping is very good
(a)
(b)

---
Vertically non-uniform dopings
Dopants are far from the channel surface
sIFM-doping scheme is accurate also looking at the single MC samples
(a)
(b)

---
Laterally non-uniform dopings
(a) (b)
Changing the doping profile along W methods are equivalent
A change in the doping profile along L modifies percolation paths
sIFM-doping better describes these last effects

---
Conclusions
The sIFM methods are a good compromise between accuracy and computational burdens allowing to explore lower probability ranges
sIFM methods are able to reproduce with a good accuracy statistical quantities
Performing a point by point comparison between sIFM results and MC reference, a non-negligible discrepancy occurs
In case of nonuniform doping profiles the accuracy of the sIFM methods should be evaluated case by case

---
Thank you for your attention
Niccolo’ Castellani,
Ph.D. Student, Politecnico di Milano, Milano (Italy)
ncastellani@elet.polimi.it

---
Effects of linearization
Inaccuracies of the sIFM schemes come from the linear approximations involved in the method

---
ID-VG of the highest sIFM-doping VT
The sIFM methods fail to reproduce filled trap ID-VG
The sIFM-doping method also fails to reproduce neutral ID-VG curve
Atomistic doping cannot be considered as a small perturbation

---
Remarks on VT dispersion
Thanks to lower computational burdens sIFM methods are useful to extend statistics to lower probability ranges
sIFM-trap:
is computationally faster
shows a better agreement with MC reference
does not introduce errors in neutral ID-VG calculation

---
Results: RTN, Uniform doping
Empty trap
Filled trap
ΔVt_MC	6,4 mV
ΔVt_sIFMdop	-66,7 mV
Ref. MC
sIFM-doping
[Speaker Notes: /prj/NEWtcad_users-data/ise_db/torrente_db/slIFM_Flash/sl_IFM_trap_RTN_drog_uniforme /prj/NEWtcad_users-data/ise_db/torrente_db/slIFM_Flash/sl_IFM_RTN_drog_uniforme /prj/NEWtcad_users-data/ise_db/torrente_db/slIFM_Flash/MC_RTN_drog_uniforme]